## Slide 1: Q3 2026 Distillation Unit Inspection Report
Detailed Findings and Action Items

## Slide 2: Detailed Findings and Action Items
Heat Exchangers (HX-101 to HX-104): No significant fouling detected. Thickness readings are within the 2mm corrosion allowance.
Piping Network (Line L-205): Minor surface oxidation observed on the external insulation cladding. Recommended for painting in Q4.
Valves and Instrumentation: Valve A-403 (HP Steam line) showed signs of micro-fissures on the upstream flange during dye-penetrant testing. The acoustic emission sensor indicated a faint internal bypass leak when fully closed.
1. Schedule immediate replacement of Valve A-403 as per SOP-MRPL-402.
2. Order 2 units of A-403 valves from vendor (Larsen & Toubro).